## Slide 1: Production of Penicillin G Potassium
Senior Design & Professionalism II
Martin Team 2
Spring 2022
Tiarra Rodrigues
Chiebuka Ejimadu
Caleb Myers
Katelynn Inman

## Slide 2: Agenda
Project Scope
Project Goals
Process Selection
Process Description
  Process Chemistry
  Overall Mass Balance
  Process Flow Diagram
  Aspen Simulation
Unit Designs
  Fermenter Design
  Fixed-bed Adsorber Design
Economic Analysis
HAZOP Analysis and Safety
  HAZOP Analysis: Fermenter
  P&ID
  Potiential hazards & Safety Precautions
  Storage & Handling
Recommendations

## Slide 3: Project Scope

## Slide 4: Penicillin G Overview
Penicillin G => Benzylpenicillin, a naturally produced antibiotic discovered in 1928
Derived from Penicillium chrysogeum fungal species but used for;
  Treating various baterical infections (Pneumonia, Strep Throat, Syphilis, etc.)
  A precursor to produce synthetic Penicillin to combat drug-resistant infections
Goal:
Design a Penicillin G Potassium plant
Produce 4% of US Demand at 99.5% purity (1.371 million kg/yr)
Operate 330 days/yr (7920 hrs)
Sell Biomass as a byproduct

## Slide 5: Chemical Properties Physical Properties
Name | Penicillin G Potassium | Color | White
Formula | C16H17KN2O4S | Odor | Odorless
Drug Class | Penicillin | Phase | Solid powder
Stability | Stable | Molecular Weight | 372.5 kg/kmol
Solubility | Soluble in Water | Density | 1.36 kg/L
Structure |  | Melting Point | 214-217 ºC

## Slide 6: Project Goals

## Slide 7: Plant Capacity
World Production – 105,000 Tons/yr (95.3 million kg/yr)
Nearly all of Penicillin G Production is in China (Assumed 90%)
US demand from China (Approximately 40% Import)
Desired Plant Capacity (Assumed 4% of US Demand)
To find Plant Capacity …
(95.3 million kg/yr * 0.9 * 0.4 * 0.04) = 1.37 million kg/yr

## Slide 8: Plant Location
Mid-point for raw materials
Large amount of agriculture and livestock for biomass sale
Average Temperature (25.8 C)
Clients
  Pfizer
  Baxter
  King Pharmaceuticals
  Sandoz

## Slide 9
Spring 2022 Gantt Chart

## Slide 10: Process Selection

## Slide 11: Process Screening: Medium Selection
A= O.1 g/L ; B= 0.2 g/L ; C= 0.3 g/L; D= 0.4 g/L ; E= 0.5 g/L; F= 0.6 g/L
Graph 2: Pen G Production with Varied Concentration of Phenylacetic Acid in Medium
Graph 1: Pen G Production with Varied Carbon Source Mediums
Lac= Lactose, Glu= Glucose, Suc= Sucrose, Mal= Maltose and PDB = Potato Dextro Agar Broth as standard medium

## Slide 12: Process Description

## Slide 13: Process Chemistry
Reaction 1 - Synthesis of Penicillin G
Reaction 2 - Synthesis of Penicillin G K from Penicillin
C12H22O11 (s) + O2 (g) + 2 C8H8O2 (s) + 4 NH3 (g) + H2SO4 (l)
C16H18N2O4S (s) + 8 H2O (l) + 2 CO2 (g) + 10 CH1.8O.5N.2 (s)
C16H18N2O4S (s) + KC2H3O2 (s) C16H17N2KO4S (s) + C2H4O2 (l)
Exothermic (ΔHrxn < 0)
Overall Reaction Mechanism
C12H22O11 (s) + O2 (g) + 2 C8H8O2 (s) + 4 NH3 (g) + H2SO4 (l) + KC2H3O2 (s)
C16H17N2KO4S (s) + C2H4O2 (l) + 8 H2O (l) + 2 CO2 (g) + 10 CH1.8O.5N.2 (s)

## Slide 14: Overall Mass Balance
INPUT = 10,400 kg/h
OUTPUT = 10,400 kg/h
Lactose = 2,190 kg/h
Oxygen = 7,350 kg/h
Phenylacetic Acid = 90 kg/h
Sulfuric Acid = 60 kg/h
Ammonia Sulfate = 660 kg/h
Potassium Acetate = 50 kg/h
Penicillin G K = 1,380 kg/h
Biomass = 1,265 kg/h
Water = 3,100 kg/h
Carbon Dioxide = 4,625 kg/h
Acetic Acid = 30 kg/h
C12H22O11 (s) + O2 (g) + 2 C8H8O2 (s) + 4 NH3 (g) + H2SO4 (l) + KC2H3O2 (s)
C16H17N2KO4S (s) + C2H4O2 (l) + 8 H2O (l) + 2 CO2 (g) + 10 CH1.8O.5N.2 (s)

## Slide 15: Block Flow Diagram
Freeze Dryer

## Slide 16
TK-001 KH2PO4 Hopper
TK-002 (NH4)2SO4 Hopper
TK-003 Yeast Extract Hopper
TK-004 Phenylacetic Acid Tank
V-001 MgSO4, 7H2O Tank
V-002 NaSO4, 7H2O Tank
V-003 ZnSO4, 7H2O Tank
V-101 Mineral Tank
PFD: Raw Material Breakdown

## Slide 17
PFD: Fermentation Process
TK-101 Lactose Hopper
V-101 Mineral Tank
V-102- V-105 Medium Tank
V-106 Inoculum Tank
R-101 – R-108 Fermenter
E-101 Heat Sterilizer
E-102 Heat Exchanger
F-101 Air Filter
C-101 Condenser
F-101

## Slide 18
PFD: Extraction Process
V-201 Rotary Vacuum Filter
V-202 Mixing Tank
V-203 Solvent Extractor
V-204 Crystallizer
V-205 Rotary Vacuum Filter
V-206 Crystal Washer
V-207 Rotary Vacuum Filter
V-208 Grinder
TK-201 Biomass Tank
TK-202 Sulfuric Acid Tank
TK-203 Butyl Acetate Tank
TK-204 Potassium Acetate Hopper
TK-205 Waste Treatment Tank
TK-206 Penicillin G Potassium Hopper
T-201 – T-206 Adsorption Tower
E-203 Freeze Dryer

## Slide 19: Aspen Simulation

## Slide 20: Unit Designs

## Slide 21: Fermenter: Design Considerations
Rules of Thumb &
Assumptions
Relevant Design Equations

## Slide 22: Fermenter Design
Reactor | 
Material | Stainless Steel
Volume | 30 m3
Pressure | 103 kPa
No. Units | 8
Operating Temperature | 30℃
Head Type | Torispherical
Diameter | 2.94 m
Height | 4.41 m
No. Baffles | 4
Baffle Width | 0.294 m
Impeller | 
Impeller Type | Rushton
No. Blades | 6
Impeller Diameter | 0.980 m
Impeller Speed | 87.7 rpm
Power | 14.1 kW

## Slide 23: Fixed-bed Adsorber: Design Considerations
Design Parameters
Lignite-based Activated Carbon Adsorption Capacity = 0.3 kg adsorbed/ kg adsorbent
Bulk Density of Lignite-based Activated Carbon = 0.55 kg/L
Total Volume =
Porosity =
Rule of Thumb
Length/Diameter = 15
Adsorbent = 80% of Adsorber Length
Maximum Adsorber Diameter = 4 m
Maximum Adsorber Length = 60 m

## Slide 24: Fixed-Bed Adsorber Design
Design Specification | 
Material | Stainless Steel
Volume | 450 m3
Packing Volume | 360 m3
Packing Material | Lignite-Based Activated Carbon
Porosity | 0.28
# of Adsorbers | 6
Operating Temperature | 2℃
Pressure | 103.4 kPa
Height of Packing | 40.27 m
Diameter of Column | 3.36 m
Height of Column | 50.33 m

## Slide 25: Economic Analysis

## Slide 26: Total Purchased Equipment Cost = $14.82 million

## Slide 27: Summary of Economics
Plant Construction = 3 years
  Total Capital Investment = $ 82.2 million
Annual Expectations
  Annual Operating Cost (100% Capacity) = $60.7 million
  Annual Sales (100% Capacity) = $114.2 million
Our plant life will last for 15 years at a capital hurdle rate of 15%, our investors should expect...
  Return on Investment = 24.3 %
  NPV (net present value) = $59.0 million
  Pay Back Period = 2.8 years
  Discounted cash flow rate of return = 23.3%

## Slide 28: Plant Cash Flow Diagram
Note:
Operating Plant Capacity at 50% at Year 1 and 90% at Year 2
Cash Flow in terms of million $

## Slide 29: HAZOP Analysis and Safety

## Slide 30: HAZOP Analysis: Fermenter
Part Considered: Fermenter | Property Keyword | Guideword | Deviation | Possible Causes | Consequences | Actions required
Medium feed | Flow | More | Overfilling | Increased Flow | Inconsistent volume | Check system parameters Add Medium consistently
 |  | Less | Underfilling | Decreased flow | Inconsistent volume | Check system parameters Add Medium consistently
Cooled Water Feed | Temperature | More | Temperature fluctuation | Increased temperature | Cooling water failure Fermenter's composition will deteriorate | Temperature controller
 |  | Less | Temperature fluctuation | Decreased temperature | Cooling water failure Fermenter's composition will not grow | Temperature controller
Inoculum Feed | Contamination | Equipment failure | Leak | Exposed to environment | Unsanitary product | Maintenance
 | Flow | No filling occuring | No flow | Equipment failure | No fermentation/growth | Inoculum added consistently

## Slide 31
Fermenter: P&ID
V-102 Medium Tank
V-103 Inoculum Tank
R-101 Fermenter (Bioreactor)

## Slide 32: Potential Hazards & Safety Precautions
In the case of:
Inhalation: move to fresh air
Skin contact: wash with soap and water
Eye contact: flush eyes as precaution
Ingestion: rinse mouth with water

## Slide 33: Storage & Handling
Stored in super sacks
Dry and refrigerated room awaiting transportation
7-day shelf life at room temperature
Stored at 4C

## Slide 34: Recommendations
The construction of this plant is proven feasible and is recommended by our team
  The plant’s annual sales ($114.2 million) exceed that of the capital and annual operating costs ($75.9 million)
  The plant is in close proximity to its necessary resources
Next steps and future recommendations
  Evaluate the economic feasibility of treating our own waste
  Explore other blade types for the fermenter that have a higher impeller efficiency

## Slide 35: Questions?????

## Slide 36: Questions?????

## Slide 37: Process Materials
 | Lactose | Phenylacetic Acid | Sulfuric Acid | Potassium Acetate | Ammonium Sulfate
Reactant/Product/Solvent | Reactant | Reactant | Reactant | Reactant | Reactant
Molecular Weight | 342.3 kg/kmol | 136.15 kg/kmol | 98.079 kg/kmol | 98.142 kg/kmol | 132.14 kg/kmol
Chemical Formula | C12H22O11 | C8H8O2 | H2SO4 | C2H3KO2 | (NH4)2SO4
Chemical Structure |  |  |  |  | 
Boiling Point | 668.9 C | 265 C | 337 C | 117.1 C | 330 C
Freezing Point | 202.8 C | 76.5 C | 10 C | 292 C | 235 C
Flash Point | 357.8 C | 132 C | - | > 250 C | -
Critical Temperature | - | - | 654 C | - | 250 C
Density | 1.76 kg/L | 1.081 kg/L | 1.83 kg/L | 1.57 kg/L | 1.77 kg/L

## Slide 38: Process Materials
 | Oxygen | Butyl Acetate | Carbon Dioxide | Acetic Acid | Water
Reactant/Product/Solvent | Reactant | Solvent | Product | Product | Product
Molecular Weights | 32 kg/kmol | 116.16 kg/kmol | 44 kg/kmol | 60.052 kg/kmol | 18.02 kg/kmol
Chemical Formula | O2 | C6H12O2 | CO2 | CH3COOH | H2O
Chemical Structure |  |  |  |  | 
Boiling Point | -183 C | 126 C | -78.46 C | 118 C | 100 C
Freezing Point | -218.79 C | -78 C | -78 C | - | 0 C
Flash Point | - | 22 C | - | 39 C | -
Critical Temperature | -118.5 C | 306 C | 31 C | 320 C | 373.9 C
Density | 1.429 kg/L | 882 kg/L | 1562 kg/L | 1.05 kg/L | 1 kg/L

## Slide 39
Fall 2021 Gantt Chart

## Slide 40: Materials & Labor
Raw Materials
  Lactose ($1.60/kg)
    $27.68 million/ year
  Ammonium Sulfate ($0.37/kg)
    $1.92 million/ year
  Sulfuric Acid ($0.09/kg)
    $0.04 million/ year
  Phenylacetic Acid ($4.60/kg)
    $3.17 million/ year
  Potassium Acetate ($1.32/kg)
    $0.49 million/ year
  Buytl Acetate ($1.12/kg)
    $8.58 million/ year
Products
  Penicillin G K ($35/kg)
    $47.99 million/ year
  Biomass ($6.62/kg)
    $66.20 million/ year
  Operating Labor Cost
    3 operators per shift
    3 shifts per day
    Operator rate, $22/hr

## Slide 41: Utilities
Process Air, compressed ($0.45/ 100 m3)
  $0.928 million/ year
Purchased Electricity ($0.045/ kWh)
  $0.129 million/ year
Waste Water Disposal ($0.53/ m3)
  $0.019 million/ year
Cooling Water ($0.08/m3)
  $0.061 million/ year

## Slide 42: Annual Operating Cost Breakdown

## Slide 43: Total Capital Investment Breakdown

## Slide 44: Net Present Value vs. Interest Rate
Discounted Cash Flow Rate of Return = 23.3%

## Slide 45: Economic Snapshot

## Slide 46: Economic Snapshot

## Slide 47: Gross Profitability
Components | Market Price (2021) | Mass Flowrate (kg/hr) | $/hr
Lactose | $1.60/kg | 2,188.7 | $3501.92/hr
Phenylacetic Acid | $4.60/kg | 87.4 | $402.04/hr
Ammonium Sulfate | $0.37/kg | 656.8 | $243.02/hr
Potassium Acetate | $1.32/kg | 46.8 | $61.78/hr
Sulfuric Acid | $0.09/kg | 58.5 | $5.27/hr
Oxygen | 0 (Air) | 7336.9 | 0 (Air)
Pen G K | $35.00/kg | 174.1 | $6093.50/hr
Biomass | $6.62/kg | 1262.7 | $8359.07/hr
Acetic Acid | $0.04/kg | 28.6 | $1.14/hr
Price of Products - Cost of Reactants = Theoretical Process Profit
$14,453.71/hr - $4,214.03/hr = $10,239.68/hr

## Slide 48: Energy Balance: Utility Equipment Table
Unit | Inlet Temp [ºC] | Outlet Temp [ºC] | Pressure [atm] | Utility | Heat flow (kJ/h) | Utility flow rate [kg/h]
E-101 (jacketed) | 25 121 | 121 25 | 2.04 | Steam Cooling water | -2.65 x 106 2.65 x 106 | 1.48 x 104 6.61 x 103
E-102 | 25 | 30 | 2.04 | Water | -1.20 x 105 | 5.75 x 103
R-101 (jacketed) | 27 | 30 | 1.02 | Cooling water | 1.00 x 107 | 5.71 x 105
E-201 | 30 | 25 | 1.02 | Cooling water | 1.89 x 105 | 9.02 x 103
E-202 | 25 | 2 | 2.04 | Calcium Chloride | 6.06 x 105 | 8.61 x 103

## Slide 49: HAZOP Analysis: Adsorption Tower
Part Considered: Absorption Tower | Property Keyword | Guideword | Deviation | Possible Causes | Consequences | Actions required
Feed from Solvent Extractor | Flow | More | Overfilling | Increased Flow | Inconsistent volume | Valve controller
 |  | Less | Underfilling | Decreased flow | Inconsistent volume | Valve controller
 |  | None | No filling occuring | No flow | Pen G is not extracted | Ensure proper liq-liq extraction takes place
 | Temperature | More | Temperature change | Increased temperature | The volatile components will react Composition deteriorates | Temperature controller
 |  | Less | Temperature change | Decreased temperature | Affects the flowrates Yields a failed production | Temperature controller
 | Contamination | Equipment failure | Leak | Exposed to environment | Unsanitary product | Maintenance

## Slide 50: Unit Balance: Fermenter
Medium = 4,829.5 kg/h
Output = 4,835.1 kg/h
Fermenter
Inoculum
KH2PO4 = 583.4 kg/h
(NH4)2SO4 = 656.8 kg/h
MgSO4*7H2O = 72.9 kg/h
Na2SO4*7H2O = 218.8 kg/h
ZnSO4*7H2O = 291.7 kg/h
Yeast Extract = 729.7 kg/h
Phenyl acetic Acid = 87.4 kg/h
Lactose = 2,188.7 kg/h
Biomass = 1,262.7 kg/h
Penicillin G = 199.4 kg/h
Water = 3,373.0 kg/h
Biomass = 5.5 kg/h
Air
Exhaust Gas
CO2 = 4,621.5 kg/h
N2 = 122,882.7 kg/h
O2 = 22,023.1 kg/h
O2 = 36,705.2 kg/h
N2 = 122,882.7 kg/h
QCW = 1.00 x 107 kJ/h
mCW = 5.71 x 105 kg/h

## Slide 51: Composition Balance
Medium = 4,829.5 kg/h
Output = 4,835.1 kg/h
Fermenter
Inoculum = 5.5 kg/h
XKH2PO4 = 0.121
X (NH4)2SO4 = 0.136
X MgSO4*7H2O = 0.015
X Na2SO4*7H2O = 0.045
X ZnSO4*7H2O = 0.060
X Yeast Extract = 0.151
X Phenyl acetic Acid = 0.018
X Lactose = 0.453
X Biomass = 0.261
X Penicillin G = 0.041
X Water = 0.698
X Biomass = 1
Air = 159,588.0 kg/h
XCO2 = 0.031
XN2 = 0.822
XO2 = 0.147
XO2 = 0.230
XN2 = 0.770
QCW = 1.00 x 107 kJ/h
mCW = 5.71 x 105 kg/h
Exhaust Gas = 149,527.3 kg/h

## Slide 52: Unit Balance: RVF
INPUT
OUTPUT
Rotary Vacuum Filter
Biomass = 1,262.7 kg/h
Penicillin G = 199.4 kg/h
Water = 3,373.0 kg/h
Biomass = 88.4 kg/h
Penicillin G = 185.4 kg/h
Water = 3,103.1 kg/h
Biomass = 1,174.3 kg/h
Penicillin G = 14.0 kg/h
Water = 269.8 kg/h
Penicillin G Recovery: 93%

## Slide 53: Unit Balance: Mixing Tank
INPUT
OUTPUT
Mixing Tank
Butyl Acetate = 844.2 kg/h
Sulfuric Acid = 58.5 kg/h
Biomass = 88.4 kg/h
Penicillin G = 185.4 kg/h
Water = 3,103.1 kg/h
Biomass = 88.4 kg/h
Penicillin G = 185.4 kg/h
Water = 3,103.1 kg/h
Sulfuric Acid = 58.5 kg/h
Butyl Acetate = 844.2 kg/h
Penicillin G Recovery: 100%

## Slide 54: Unit Balance: Solvent Extractor
INPUT
OUTPUT
Solvent Extractor
Penicillin G Recovery: 86%
Butyl Acetate = 844.2 kg/h
Sulfuric Acid = 58.5 kg/h
Biomass = 88.4 kg/h
Penicillin G = 185.4 kg/h
Water = 3,103.1 kg/h
Butyl Acetate = 759.8 kg/h
Biomass = 3.5 kg/h
Penicillin G = 159.5 kg/h
Water = 155.2 kg/h
Butyl Acetate = 84.4 kg/h
Sulfuric Acid = 58.5 kg/h
Biomass = 84.9 kg/h
Penicillin G = 26.0 kg/h
Water = 2948.0 kg/h

## Slide 55: Unit Balance: Carbon Treatment
INPUT
OUTPUT
Carbon Treatment
Butyl Acetate = 759.8 kg/h
Biomass = 3.5 kg/h
Penicillin G = 159.5 kg/h
Water = 155.2 kg/h
Butyl Acetate = 3,450.7 kg/h
Penicillin G = 159.5 kg/h
Water = 150.5 kg/h
Butyl Acetate = 38 kg/h
Biomass = 3.5 kg/h
Water = 4.7 kg/h
Penicillin G Recovery: 100%

## Slide 56: Unit Balance: Crystallizer
INPUT
OUTPUT
Crystallizer
Penicillin G K Recovery: 100%
Acetic Acid = 143.3 kg/h
Butyl Acetate = 3838.3 kg/h
Penicillin G K = 888.7 kg/h
Water = 752.9 kg/h
Potassium Acetate = 234.3 kg/h
Butyl Acetate = 387.7 kg/h
Butyl Acetate = 3,450.7 kg/h
Penicillin G = 797.8 kg/h
Water = 754.9 kg/h

## Slide 57: Unit Balance: Crystal Filter 1
Crystal Filter
Butyl Acetate = 460.6 kg/h
Penicillin G K = 879.8 kg/h
Water = 37.6 kg/h
Acetic Acid = 143.3 kg/h
Butyl Acetate = 3377.7 kg/h
Penicillin G K = 8.9 kg/h
Water = 715.3 kg/h
Penicillin G K Recovery: 99%
Acetic Acid = 143.3 kg/h
Butyl Acetate = 3838.3 kg/h
Penicillin G K = 888.7 kg/h
Water = 752.9 kg/h

## Slide 58: Unit Balance: Crystal Washing
INPUT
OUTPUT
Crystal Washing
Butyl Acetate = 690 kg/h​
Penicillin G K = 879.8 kg/h​
Water = 37.6 kg/h
Butyl Acetate = 460.6 kg/h
Penicillin G K = 879.8 kg/h
Water = 37.6 kg/h
Butyl Acetate = 229.4 kg/h
Penicillin G K Recovery: 100%

## Slide 59: Unit Balance: Crystal Filter 2
INPUT
OUTPUT
Crystal Filter
Butyl Acetate = 82.8 kg/h​
Penicillin G K = 871 kg/h​
Water = 1.9 kg/h
Butyl Acetate = 607.2 kg/h
Penicillin G K = 8.8 kg/h
Water = 35.8 kg/h
Butyl Acetate = 690 kg/h​
Penicillin G K = 879.8 kg/h​
Water = 37.6 kg/h
Penicillin G K Recovery: 99%

## Slide 60: Unit Balance: Freeze Dryer
INPUT
OUTPUT
Vacuum Drying
Butyl Acetate = 82.7=8 kg/h
Penicillin G K = 871 kg/h
Water = 1.9 kg/h
Butyl Acetate = 78.6 kg/h
Water = 1.8 kg/h
Butyl Acetate = 4.1 kg/h
Penicillin G K = 871 kg/h
Water = 0.07 kg/h
Penicillin G K Recovery: 100%

## Slide 61: Fermenter Design: Calculating Volume

## Slide 62
Gantt
Chart

## Slide 63
Gantt Chart (Graph)