## Slide 1: HW Chemical Production of Sulfuric acid
Martin Team 5
Taylor Linton, Tyecia Franklin, Wasil Mahmood, Franck Nangomoko

## Slide 2: Outline
Project Scope
Gantt Chart
Plant Metrics
Process Flow Diagram
Aspen Simulation
Equipment Design
Material and Energy Balance
Process Safety and Controls
Economic Analysis
Conclusion

## Slide 3: Project Scope
Problem Statement: Design a sulfuric acid plant for the production of fertilizer grade sulfuric acid
Project Deliverables:
Justification of plant location and capacity
Process Flow Diagram
Detailed Equipment Design
Complete HYSYS/ASPEN simulation
Process Safety & HAZOP Analysis
Detailed Economic Analysis

## Slide 4: Gantt Chart

## Slide 5: Plant Capacity
Production:
  340 days
  8,160 hrs/yr
  800,000 tons/yr
  1,763,696,000 lb/yr
Customer​ | Annual Capacity(MTPA)​
Ioneer | 1,190,000​
Mosaic Company | 986,000
Potash Corp | 850,000​
Our Plant | 800,000
Simplot Company​ | 756,000​
Mosaic Company​ | 648,000​
Freeport-McMoRan Copper & Gold Inc. | 527,000

## Slide 6: Plant Location
Location: Hopewell, FL​
Reasoning: Close to phosphate fertilizer plants​
Customers:​
  CF Industries- Plant City​
  Mosaic Company- New Wales​
  Mosaic Company- Bartow ​
  Phosphoric Acid Team- Plant City​
​

## Slide 7: Process Flow Diagram

## Slide 9
TK-100
Sulfur
Storage Tank
H-100
Sulfur Burner
S (l) + O2 (g) →SO2 (g)
R-100
Packed Bed Reactor
T-100
Absorption
Tower #1
H-101
Boiler
SO2 (g)+ ½O2 (g)→ SO3 (g)

## Slide 10
SO3 (g) + H2SO4 (l) → H2S2O7 (l)
Oleum
T-100
Absorption
Tower #1
T-101
Absorption
Tower #2
TK-101
Dilution Tank
TK-103
Sulfuric Acid
Storage Tank
TK-102
Purified Water Storage Tank
H2S2O7 (l) + H2O (l) → 2H2SO4 (l)
Oleum

## Slide 11
35
9
SO2 from T-101 is recycled into leading into R-100

## Slide 12: Equipment Design & Material and Energy Balance

## Slide 13: Overall Material Balance
SO3(g) + H2SO4(l) H2S2O7(l)
OVERALL MASS BALANCE
S(l) + O2(g) SO2(g)
SO2(g) + 0.5 O2(g) SO3(g)
SO2(g) + 0.5 O2(g) + H2O(l) H2SO4(l)
Main Reactions
H2S2O7(g) + H2O(l) 2H2SO4(l)

## Slide 14: Material and Energy Balance

## Slide 15: Material and Energy Balance

## Slide 16: ASPEN SIMULATION
16

## Slide 17: Packed Bed Reactor R-100
R-100

## Slide 18: Reactor Specifications
Relevant Design Equations
Pressure Drop Ergun Equation

## Slide 19: Absorption Tower t-101
Click to add text

## Slide 20: Absorption Tower Specifications
Relevant Design Equipment
Component balance
Kremser Equation for theoretical stages
20

## Slide 21: Process Safety & Controls

## Slide 22
Study Node | Property | Deviation (guideword) | Cause | Consequence | Action
Absorption Tower #2 | Flow | No | Closed S03 Valve Closed oleum valve Closed H2SO4 valve Closed SO2 valve | Input concentrated sulfuric acid leaves through oleum outlet Tower filled with oleum, causing possible flooding. SO3 leaves through SO2 outlet. Constant pressure increase within tower, leading to rupture. | Flow indicator (FI-101, FI-102, FI-103) installation Installation of tower liquid level sensor System manual bypass requirement to activate tower without opening of valves.
 |  | More | SO3 compressor malfunction Concentrated H2SO4 pump malfunction | High flow of SO3 leading to increased pressure within vessel causing rupture. High flow of concentrated H2SO4 In causing tower flooding. | Pressure indicator (PI-101) and pressure transmitter (PT-101) linked to SO3 control valve (PC-101) Flow indicator (FI-101, FI-102,) installation Flow controller (FC-101) linked to FI-102 to regulate sulfuric acid input.
 |  | Less | Partially closed S03 Valve Partially closed oleum valve Partially closed H2SO4 valve Partially closed SO2 valve | Leftover H2SO4 leaving through oleum output line Tower filled, with possible back flow Excess SO3 leaves through SO2 outlet line Pressure increase in tower | Flow indicator (FI-101, FI-102, FI-103) installation Tower liquid level control system (LE-101, LT-101, LIC-101)
 | Temperature | More | Malfunction of SO3 cooling heat exchanger | Tower temperature above established parameters | Installation of temperature indicators (TI-101,TI-102,TI-103) TIC-101 connected to cooling water valve.
 |  | Less | Above | Tower temperature below established parameters | Above
 | Pressure | More | SO3 input line compressor malfunction. S02 output line blockage | Tower pressure above established parameters | Pressure transmitter (PT-101) linked to SO3 control valve (PC-101)and PSV (PC-102) Implementation of pressure parameter alarm.
 |  | Less | SO3 input line compressor malfunction. Possible tower leak SO2 output line leak | Tower pressure below established parameters | Above
Hazard Analysis: Absorption Tower

## Slide 23: P&ID: Absorption tower #2

## Slide 24: Safety Considerations: NFPA

## Slide 25: Safety Considerations
Compound​ | Concerns​
H2SO4​ (sulfuric acid)​ | Clear, colorless, oily liquid (may turn yellowish to amber upon aging)​​ Aggressive oxidizer (can create highly flammable hydrogen gas if it is spilled on metals)​ (Heavy compound) static load pressure constantly pressing against the bottom third of the storage tank​
H2S7O7​ (oleum)​ | Corrosiveness decreases with increasing SO3 content.​ Low oleum velocities recommended to reduce piping corrosion​
SO3​ (sulfur trioxide)​ | Reacts explosively with water (high heat of reaction)​ High reactivity with organic compounds​

## Slide 26: Safety Considerations: PPE
PPE
Class D: for minimal risk of exposure | Safety glasses with side shields Steel-toe safety shoes with PVC, neoprene, or composite soles Pants and sleeved shirt, or coveralls, made of acid-resistant polyester, acrylic or wool Hard hat
Class C: for moderate risk of exposure | Coverall splash goggles (a face shield can be added over the goggles if desired, but is not a replacement for goggles) Acid-resistant gauntlet gloves Optional, acid-resistant jacket Optional, face shield
Class B: for elevated risk of exposure | Head Protection: splash hood and hard hat (limit duration of tasks to avoid oxygen deficiency in hood) Eye Protection: chemical splash goggles Respiratory: not required for non-fuming sulfuric acid Hand Protection: acid-resistant gauntlet length gloves with sleeves over gloves Body Protection: acid suit, 1 piece or 2 pieces (fabric must pass ASTM testing for ≥ 93% sulfuric acid) Foot Protection: acid-resistant boots with pant legs over boots
Class A: or maximum risk of exposure, used during an emergency leak/spill situation | Hard hat Eye Protection: full face mask Respiratory: NIOSH approved respiratory protection Body Protection: acid-resistant, fully encapsulated suit (Fabric must pass a 45 min breakthrough ASTM F739 chemical permeation test for ≥ 93% Sulfuric Acid) Foot Protection: acid-resistant boots with pant legs over boots

## Slide 27: Economic Analysis

## Slide 28: Equipment Summary
Unit | Unit Description | Cost | # of Units | Total Cost
P-100 | Feed Pump | $10,400 | 2 | $20,800
TK-100 | Sulfur Storage Tank | $576,000 | 3 | $1,728,000
P-101 | Reciprocating Pump | $9,000 | 2 | $18,000
C-100 | Centrifugal Compressor | $260,500 | 2 | $561,000
C-101 | Rotary Compressor | $227,500 | 2 | $455,000
P-102 | Centrifugal Pump | $41,900 | 2 | $20,950
H-100 | Furnace | $7,930,000 | 1 | $7,930,000
H-101 | Packaged Steam Boiler | $2,090,000 | 1 | $2,090,000
C-102 | Centrifugal Compressor | $414,500 | 2 | $829,000
E-100 | Multiple Pipe Heat Exchanger | $36,900 | 1 | $36,900
R-100 | Packed Bed Reactor | $286,000 | 2 | $572,000
E-101 | Multiple Pipe Heat Exchanger | $10,500 | 1 | $10,500
E-102 | Double Pipe Heat Exchanger | $5,200 | 1 | $5,200
E-103 | Double Pipe Heat exchanger | $5,830 | 1 | $5,830

## Slide 29: Equipment Summary
Unit | Unit Description | Cost | # of Units | Total Cost
E-104 | Shell and Tube Heat Exchanger | $62,500 | 1 | $62,500
T-100 | Absorbing Tower 1 | $324,000 | 1 | $324,000
P-103 | Reciprocating Pump | $12,150 | 2 | $24,300
TK-101 | Dilution Tank | $75,000 | 1 | $75,000
P-104 | Reciprocating Pump | 12,100 | 2 | $24,200
T-101 | Absorbing Tower 2 | $54,800 | 1 | $54,800
P-105 | Reciprocating Pump | $24,100 | 2 | $24,100
TK-103 | Purified Water Tank | $54,800 | 1 | $54,800
P-106 | Reciprocating Pump | $10,250 | 2 | $20,500
TK-104 | Sulfuric Acid Storage Tank | $576,000 | 1 | $576,000
C-103 | Rotary Compressor | $40,850 | 2 | $81,700
C-104 | Centrifugal Compressor | $820,000 | 2 | $1,640,000
C-105 | Rotary Compressor | $39,250 | 2 | $78,500
V-100 | Vacuum Pressure Swing Adsorption | $1,500,000 | 1 | $1,500,000

## Slide 30: Cost Analysis
Description | Value
Plant Capacity (lb/yr) | 1,763,696,000
Return on Investment (%/y) | 36.1
Payback Period | 1.9
Net Present Worth (million) | 155.38
Discounted Cash Flow Rate of Return(%/y) | 15.2
Raw Materials
  Sulfur- $0.10/kg
  Water- $0.002/kg
  Oxygen- $0/kg
Catalyst
  Vanadium Pentoxide-$112.64/kg
Product
  Sulfuric Acid- $0.24/kg
Material Pricing

## Slide 31
Direct Costs |  | 
Item | Fluid Processing Plant Fraction | Calculated Value ($millions)
Purchased equipment, E' |  | 20.900
Delivery, fraction of E' | 0.10 | 2.090
Subtotal: delivered equipment |  | 22.990
Purchased equipment installation | 0.47 | 10.805
Instrumentation &Controls(installed) | 0.36 | 8.276
Piping (installed) | 0.68 | 15.633
Electrical systems (installed) | 0.11 | 2.529
Buildings (including services) | 0.18 | 4.138
Yard improvements | 0.10 | 2.299
Service facilities (installed) | 0.70 | 16.093
Total direct costs | 2.60 | 82.764
Indirect Costs |  | 
Engineering and supervision | 0.33 | 7.587
Construction expenses | 0.41 | 9.426
Legal expenses | 0.04 | 0.920
Contractor's fee | 0.22 | 5.058
Contingency | 0.44 | 10.116
Total indirect costs | 1.44 | 33.106
Fixed capital investment (FCI) |  | 115.870
Fixed Capital Investment
31

## Slide 32
Item | Cost, million $/y
Raw materials | 37.413
Operating labor | 0.885
Operating supervision | 0.133
Utilities | 2.034
Maintenance and repairs | 7.141
Operating supplies | 1.071
Laboratory charges | 0.133
Royalties (if not on lump-sum basis) | 0.655
Variable cost = | 49.465
Item | Cost, million $/y
Plant overhead, general | 4.895
Plant Overhead = | 4.895
Administration | 1.632
Distribution & selling | 3.273
Research & Development | 2.618
General Expenses = | 7.523
Item | Cost, million $/y
Taxes (property) | 2.380
Insurance | 1.190
Fixed Charges = | 3.571
Manufacturing cost = | 57.931
Production Cost
32

## Slide 33: Plant Cash Flow Diagram
Initial Investment: $115,000,000

## Slide 34: Conclusion
Plant Capacity: 800,000 tons/ year
Market: Fertilizer
Location: Hopewell, FL
Product: 98% sulfuric acid
Economics
  Payback Period- 2 years
  Positive return on investment

## Slide 35: acknowledgements

## Slide 36: Questions

## Slide 37: Extra Slides

## Slide 38: Vacuum Pressure Swing Adsorption
Each adsorber undergoes a cyclic process, consisting of:
→ Adsorption (O₂ production)
→ Desorption (evacuation)
→ Re-pressurization (pressure build-up)

## Slide 39: Storage and Handling
3 Available Storage Material Options
    Steel (good for < 98%)
    Fiberglass reinforced plastic (FRP)
    Polyethylene or cross-linked polyethylene
Figure 1: FRP Tank
Figure 2 : Steel Tank
Figure 3: Polyethylene Tank

## Slide 40: Process Selection
Process​ | Raw Materials​ | Description​ | Advantages​ | Disadvantages​
Sulfur Burning​ | Elemental sulfur​ | - 70% of world production​ - burn sulfur with dry air​ | - requires little attention​ | - ​
Metallurgical​ | metal sulfide ores and smelter gas burning​ | - 20% of world production​ -smelting metal sulfide concentrates​ | - removes SO2 from smelting and roasting off gases​ | -requires large and expensive​ equipment​
Acid Regeneration​ | Spent sulfuric acid ​ ​ | - 10% of world production​ - sulfuric acid is decomposed by a furnace​ | - makes useful product from waste​ | - high transportation cost​ -produce transportation emissions​

## Slide 41: Production Materials
Alloy​ | Conditions​
C-20, 20-Cb3​ | •Can handle ambient and slightly elevated temperatures​ •Can handle H2SO4 at any concentration​
C-276, C-22, 59​ | •Can handle H2SO4 at any concentration​ •Ideal for higher temperatures​
Lewmet 55, Lewmet 66​ | •Ideal for pump parts, screens, nozzles, etc.​ •Sulfuric acid resistant​
Carbon Steel​ | •Ideal for oleum equipment and piping​ •Corrosiveness decreases with increasing SO3 content.​
Gray Cast-Iron​ | •Ideal for sulfuric acid piping​ •Low price​ •Lifespan 7-15 years​

## Slide 42: Uses
Pharmaceutical: It is used as a solvent for the chemical synthesis of a variety of chemical substances including active pharmaceutical ingredients. One type of active pharmaceutical ingredients manufactured by using sulphuric acid are the alkylating agents which are commonly used in the chemotherapy
Steel Manufacturing: Sulphuric acid is used in the processing of iron, copper and steel to clean the metal and prevent oxidation before it is plated with tin or zinc
Water treatment: It is frequently used to bring the pH level of wastewater back to normal

## Slide 43: Market Analysis
Target Market Percentage: 30%